## Slide 1: FTD Basics
Dax Mickelson
dmickels@cisco.com
Training around FTD version 6.1 release
This presentation can be downloaded from: http://tinyurl.com/ftdclass
Password is: FTDFERoadshow

## Slide 2
Logistics
Bathrooms
Coffee/Water/Drinks
Internet Access
Day 1
9AM: Lecture
10AM-Noon: Lab
Noon-1PM: Lab and lunch
1PM-2PM: Lecture
2PM-6PM: Lab
Day 2 (rinse, repeat)
9AM: Lecture
10AM-Noon: Lab
Noon-1PM: Lab and lunch
1PM-2PM: Lecture
2PM-6PM: Lab

## Slide 3
Lecture Format
1 hour lecture followed by a 10 minute break.
Rinse, repeat (This is a 4 hour lecture so 4 one-hour sections with 3 ten-minute breaks.)
Use Q&A to ask questions and the panelists will respond.
Lab Format
Your lab will either start directly after this lecture or it will start on Wednesday February 1st. Check your invite to figure out which is for you.

## Slide 4: Agenda
Introduction to NGFW
Delivery Options
Licensing
FTD Intro and Benefits
FTD Initialization and Mgmt Config.
FTD Configuration Options
FTD to FMC Registration
FTD Deployment Modes
FTD Security Zones
NAT on FTD
Access Control Policy
ACP Rules
URL Filtering
SafeSearch / YouTube
Malware & File Policy
SSL Policy
Intrusion Policy
Rate Limiting
Network Discovery
FTD Packet Flow
Reports and Reporting
VPN on FTD
API
Upgrade ASA to FTD Code
Set up Firepower Device Manager
Cisco Healthcheck & Tuning Services
Questions?

## Slide 5: NGFW: What it is and why its important

## Slide 6: Traditional Security
Firewall
  Security Levels
  ACLs using L3/L4 protocol
  NAT
IPS
  Inline or “to the side”
  Use signatures to detect patterns

## Slide 7: Traditional Security (cont.)
ICMP tunnels
DNS tunnels
Reverse SSH tunnels
Communication with Command and Control servers
HTTP is the new TCP

## Slide 8: Marriage of Firewall and IPS -- NGFW
Tight integration of ASA firewall and Firepower (SNORT) IPS.
Regular updates of signatures and lists from Cisco Talos and other security monitors.

## Slide 9: Introduction to NGFW
  World’s most widely deployed, enterprise-class ASA stateful firewall
  Granular Cisco® Application Visibility and Control (AVC)
  Industry-leading FirePOWER next-generation IPS (NGIPS)
  Reputation- and category-based URL filtering
  Advanced malware protection
Cisco ASA
Identity-Policy Control & VPN
URL Filtering
(Subscription)
FireSIGHT
Analytics & Automation
Advanced Malware Protection
(Subscription)
Application Visibility & Control
Network Firewall
Routing | Switching
Clustering & High Availability
WWW
Cisco Collective Security Intelligence Enabled
Built-in Network Profiling
Intrusion Prevention (Subscription)

## Slide 10: Delivery Options

## Slide 11: NGFW Delivery Options
Hardware:
ASA with FirePower Services
ASA and FirePOWER (independent servers)
Firepower Threat Defense (FTD)
Virtual Machine:
ASAv and Firepower Virtual Appliance (independent VMs)
vFTD

## Slide 12: Licensing

## Slide 13: Licensing

## Slide 14: Licensing (cont.)

## Slide 15: Firepower Threat Defense (FTD): Introduction and Benefits

## Slide 16: Evolution of NGFW

## Slide 17: Current NGFW – Rough Packet Flow
Ingress to firewall
Copy packet to IPS for inspection
  Serialization delay of packet
  Down protocol stack in firewall and backup stack in IPS
Copy packet back to firewall
  Serialization delay of packet and result
  Down protocol stack in IPS and backup stack in firewall
Egress firewall

## Slide 18: FTD– Rough Packet Flow
Ingress into server put into memory. Memory point sent to firewall process.
Firewall process runs checks against packet at that memory pointer and then sends memory pointer IPS process.
IPS process runs checks against packets at that memory pointer and sends result to firewall process.
Firewall process sends packet to server for egress.

## Slide 19: Firepower Threat Defense (FTD): Initialization and Configuration

## Slide 20: Management NIC
Must use Management Interface for configuration.
No CLI config mode – for data plane.
Management NIC in “VRF”.

## Slide 21: Deploy FTD (virtual machine)

## Slide 22: OVA with Configuration Wizard

## Slide 23: Management NIC Configuration

## Slide 24: Management NIC Configuration (cont.)
Note: There is no “restarting” or “rerunning” the configuration wizard. You’ll have to use the CLI commands that start with configure network to change the management NIC’s configuration.

## Slide 25: FTD CLI
3 “shells” that you can access:
FTD shell (AKA CLISH) – “>”
Linux shell (AKA BASH)
  Non-root – “$”
  Root – “#”
ASA Shell (AKA Lina CLI) – “firepower>”

## Slide 26: FTD Configuration Options: FMC vs. Firepower Device Manager

## Slide 27: Data Plane Configuration Options
Firepower Management Center
Firepower Device Manager
Firepower Management Center (FMC): Centralized server for managing multiple devices
Firepower Device Manager: On-box manager for a single FTD device. (5500-X Hardware only.)

## Slide 28: Firepower Device Manager
Not as feature rich as FMC, especially in reporting.
Supported Features as of v6.1:
  NAT
  Routing
  Access Control
  Device and Event Monitoring
  Easy Device Setup
Roadmap:
  Site to Site VPN
  Security Intelligence
  SSL, Identity, Rate Limiting (QoS), etc.
  Active/Passive Authentications
No Current Plan:
  Threat Intelligence and Analytics
  Risk Reports
  Correlation and Remediation

## Slide 29: Firepower Management Center (FMC)
Centralize manager that allows common configuration across several devices.
  Configure once, deploy to many.
Doesn’t manage ASA.
Manages Firepower and FTD devices.
Communicates with managed device via TCP/8305.
Can receive updates via “cloud” services, such as Cisco Talos.
  Offline update available too if direct INET access not allowed.

## Slide 30: FTD to FMC Registration

## Slide 31: FMC Registration
FMC can be L2 adjacent or separated via L3.
Management NIC needs a route to the FMC though (aside from the data plane configuration).
Use CLI command configure manager add (with options) to configure FTD to register with FMC.
FMC needs configure to know about this FTD box too (no auto registration).
FTD connects to FMC on TCP/8305.

## Slide 32: FMC Registration (cont.)
What about remote FTDs though?
Have pre-existing L3 route (maybe via MPLS) to FMC.
Pre-stage FTD in a development network and have FMC communication go over VPN or some such.  DANGEROUS!!!
Put the Management NIC on the Public Internet.
Use Firepower Device Manager (single box management).
Where to cable the Management NIC?

## Slide 33: Static IP on Management NIC
Configure outbound access for FMC through existing edge device.
  No static NAT entry required in this configuration.
Cable and configure Management NIC on INET side.
  Use a static IP issued from ISP.
Issue the command configure manager add DONTRESOLVE <shared key> <NAT ID> on FTD’s CLI.
Add FTD into FMC
  Host: Static IP of FTD’s Management NIC.
  Registration Key: <shared key>
  NAT ID: <NAT ID>
The FMC will then attempt to establish communication with FTD and the registration process will ensue.

## Slide 34: DHCP IP on Management NIC
Configure static NAT entry and outbound access for FMC through existing edge device.
Cable and configure Management NIC on INET side.
  Use a DHCP IP issued from ISP.
Issue the command configure manager add <static NAT IP of FMC> <shared key> <NAT ID> on FTD’s CLI.
Add FTD into FMC
  Host:
  Registration Key: <shared key>
  NAT ID: <NAT ID>
The FTD will then attempt to establish communication with FMC and the registration process will ensue.

## Slide 35: FTD Deployment Modes

## Slide 36: FTD Deployment Modes
FTD is built to be a firewall thus:
Routed
Transparent
Notes:
  No multiple context mode available on FTD today.
  Routed or transparent mode configured with setup dialog.
    Changing between these modes requires re-registering with FMC.
    Policies will be re-deployed.
Optional interface modes can be in these IPS/IDS modes:
Inline
Inline Tap
Passive

## Slide 37: FTD Deployment Modes (cont.)
Routed – The traditional mode of the firewall.
  Two or more interfaces that separate L3 domains.
  The FTD is the Router and Gateway for local hosts.
  Static routes, RIP, OSPF, and BGP are supported.
  Fail-open is NOT supported.
10.1.1.0/24
192.168.1.0/24
192.168.1.1
10.1.1.1
IP:192.168.1.100 GW: 192.168.1.1
NAT
DRP

## Slide 38: FTD Deployment Modes (cont.)
Transparent Mode is where the firewall acts as a bridge functioning at L2.
  Transparent mode firewall offers some unique benefits in the DC.
  Transparent deployment is tightly integrated with our ‘best practice’ data center designs.
192.168.1.0/24
192.168.1.1
IP:192.168.1.100 GW: 192.168.1.1
VLAN192
VLAN1920

## Slide 39: IPS/IDS Modes
“Extract” a few of the FTD device’s interfaces from firewall mode and apply IPS/IDS mode.
Traffic process by minimal ASA functions and all SNORT processes.
Packet not impacted in Inline Tap or Passive modes but could be dropped either by ASA or SNORT in Inline mode.

## Slide 40: Inline Mode
Two physical interfaces paired together.
Paired interfaces must be assigned to an inline set.
  Bump in the wire, entirely transparent to the network.
  Easy to insert into an existing network.
  Multiple pairs can be configured on same sensor as sets.

## Slide 41: Inline Tap Mode
Same as Inline but packets are never dropped.
Used for evaluating and tuning of rules.

## Slide 42: Passive Mode
IDS mode
Separate device must send copies of the packets.
  SPAN (or monitor) from a switch.
  Network Taps.
One or more physical ports designated as passive.
Only copies of the packets are sent to the sensor.
Does NOT impact network traffic.
Easy to insert into an existing network.
Optionally integrate with ISE to remediation recommendations.

## Slide 43: Multi-Featured NGFW
Routed / Transparent for firewall mode. (5, 6, 7)
IDS
  Passive interface for monitoring copied packets from SPAN port. (4)
IPS
  Inline pair to inspect traffic and take action. (0, 1)
  Inline tap to inspect traffic but not take action. (2, 3)

## Slide 44: FTD Security Zones

## Slide 45: Security Zones vs. Security Levels
Security Levels are like waterfalls with one interface having a higher “level” and thus more secure than another interface.
Security Zones are like fences by dividing interfaces into “like groups” and establishing the rules for crossing the fence line.

## Slide 46: FTD Security Zones
True zone-based firewall
Security Zones are collections of interfaces or sub-interfaces
Policy rules can apply to source and/or destination security zones
Security levels are not used

## Slide 47: Configuring Security Zones Considerations
Common Configuration:
“Inside” and “Outside” zones deployed to all devices.
Unique Per Site:
Unique zone name for each zone at each location.
Hybrid:
Some names are unique (such as DMZ) and other zones are common at all sites.

## Slide 48: NAT on FTD

## Slide 49: Network Address Translation
Two “types” of NAT in FTD devices: Auto-NAT and Manual NAT
Auto-NAT, also known as Object-NAT or Host NAT.
  Defined within an object.
  Just translates the source IP or IP range.
  Can be a static or dynamic NAT. (Think 1:1 NAT or PAT.)
Manual NAT, also known as Twice-NAT.
  Can specify the source and destination addresses for NAT.

## Slide 50: Network Address Translation (NAT)
NAT Policy
  FTD Policies vs. Firepower Policies
  Associated with Devices
  Contains rules (edit policy to see rules)
A single NAT Policy can be applied to more than 1 device (think common policy for a group of FTD devices).

## Slide 51: Network Address Translation (NAT) (cont.)
NAT Rule
  Various settings to specify source/destination interfaces, IP addresses, Ports, etc.
  Can be “Manual” or “Auto”. (More about these later.)

## Slide 52: Network Address Translation (NAT) (cont.)
NAT order of operations:
Section 1 and 3 rules are manually ordered. (i.e. The administrator orders them.)
Section 2 (i.e. Auto-NAT rules) are ordered Static NAT before Dynamic NAT and then within each of those categories Longest to Shortest Prefix.

## Slide 53: Configuring NAT Considerations
Common Configuration:
“Inside” to “Outside” PAT.
Unique Per Site (kind of):
Static NAT for a specific host between two security zones.
PAT using something other than “interface” IP.
Note: NAT configuration will be deployed to all devices that use the security zones listed in the NAT rules.

## Slide 54: Access Control Policy (ACP)

## Slide 55: Access Control Policy (ACP)
An ACP is the collection/association point for MANY of the other policies and rules. (Think of an ACP as the gateway to applying policy to a device.)
1:N -- A single ACP can be assigned to multiple devices but a device can only be associated with one ACP.
Supports nesting/inheritance of ACPs.

## Slide 56: Access Control Policy (cont.)
Policy Types:
Access Control Rule – Specify, inspect, and log network traffic
  URL Filtering – Not a separate policy but configured within an Access Control Policy rule.
Intrusion – Inspect traffic for security violations
Malware & File – Detect and inspect files for malware
SSL – Inspected encrypted traffic
DNS – Controls whitelisting and/or blacklisting of traffic based on DNS
Identity – Collect identity information via captive portal
Prefilter – Early handling of traffic based on L1-L4 criteria

## Slide 57: Access Control Policy (cont.)

## Slide 58: Creating an ACP
The Name and Default Action are required. All other fields are optional.

## Slide 59: Access Control Policy (cont.)
Policy is applied on a per device basis (though multiple devices can be associated to the same policy).
Specifies a “Default Action”. (What to do if no rules apply.)
Uses an interesting inheritance association between access control policies.

## Slide 60: Access Control Policy (cont.)
Nested Access Control Policies.
A device can only be “directly” associated with one Access Control Policy but can get other policy’s rule via inheritance.

## Slide 61: Access Control Policy (cont.)
There is a LOT more to Access Control Policies:
Security Intelligence
HTTP Responses
MANY Advanced features: SSL Policy, Prefilter Policy, Variable Set, Intrusion Policy, etc.

## Slide 62: ACP Rules

## Slide 63: Access Control Rules

## Slide 64: ACP Rules
A rule can match against Source/Destination Zones, IP, Ports, as well as VLAN or Security Group tags, and so much more!
A rule is also where you associate which File inspection, Intrusion/SNORT inspection, and what type of logging to do.

## Slide 65: Access Control Policy (cont.)
Within an Access Control Policy rules are sorted into two sections: Mandatory and Default
Mandatory rules are checked first (top down) and then Default rules (top down).

## Slide 66: Access Control Policy (cont.)
Rules still process Mandatory prior to Default but notice that the “parent” sections sandwich the “child” sections.
Where would you put a rule to be applied no matter what any child policy rules states?
Where would you put a rule that should be used if no child policy has a rule that matches?

## Slide 67: Access Control Policy (cont.)
When should we use the Default Action?
Should we log events that hit it?
What should the action be: Block, Trust, Discovery, Permit?
Finally, bear in mind the “Default Action”. The action used when no other rule matches the packet flow.

## Slide 68: Configuring ACP and ACP Rule Considerations
Common Configuration:
Don’t permit traffic sourced from non-company IP address ranges outbound?
Common “Default Action”?
Unique or Subset Configuration:
Sort devices by “location type” (i.e. HQ, branch, DC, etc.) and apply ACP rules to each location type.

## Slide 69: Access Control Policy (cont.)
ACP Rules are applied directly to an ACP.

## Slide 70: URL Filtering

## Slide 71: Minimize your exposure to web-based threats
Restrict categories of URLs
Filter out over 280 million URLs based on any of the 80+ categories into which they are grouped; new URLs are added daily
Block specific URLs
Restrict access to specific sites and subsites
bad_url.com
office365.com
Social Media

Gambling

Health

Drug Use

Gaming

Change policies easily
Use the refined user interface to make additions or changes with just a few clicks
Allowed
Restricted

## Slide 72: Licensing

## Slide 73: URL Filtering
Filter based on Category and/or Reputation, or via a specific URL (an object manually created, a list of URLs, or an automatically updated list of URLs).
Note: To use category and/or reputation requires URL License.

## Slide 74: URL Filtering (cont.)
Select a category and then optionally choose a reputation.
Notice how any reputation score equal to or higher is also selected.
Uses Cisco Security Intelligence to define what URLs match these categories and reputations.

## Slide 75: URL Object
A URL object defines a single URL or IP address
Performs a simple substring match
Disregards the protocol (HTTP/HTTPS)

## Slide 76: URL List and Feed
A URL list is a text file of specific URLs
A URL feed is a continuously updated list of URLs

## Slide 77: Access Control Policy -- Revisited
URL Filtering is applied within an ACP Rule.

## Slide 78: Malware & File Policy

## Slide 79: Malware & File Policies
Malware = AMP
Controls what and how files are allowed, blocked, and inspected
Simple policy applies the same action (Malware Cloud Lookup) to all files
Actions are:
  Detect Files: Detect and log the file transfer, perform no inspection
  Block Files: Block and log the file transfer, perform no inspection
  Malware Cloud Lookup: Inspect the file to determine disposition (Malware, Unknown, or Clean) and log
  Block Malware: Inspect the file to determine disposition, log and block if Malware
Inspection includes static analysis of the file (via Spero), dynamic analysis (via AMP Threat Grid), and local analysis (via ClamAV)
Complex policies can include different actions and levels of inspections for different application protocols, directions, and file types.

## Slide 80: Licensing

## Slide 81: Malware & File Use Case
Block malicious Office, Executable, and PDF files transferred over HTTP

## Slide 82: Malware & File Use Case (cont.)
Block malicious Office, Executable, and PDF files transferred over HTTP

## Slide 83: Malware & File Use Case (cont.)
Block malicious Office, Executable, and PDF files transferred over HTTP
Blocks all files matching policy file type(s)
Detection only
(no blocking)

## Slide 84: Malware & File Use Case (cont.)
Block malicious Office, Executable, and PDF files transferred over HTTP
Stores files on sensor for further investigation by analyst
Spero = Static Analysis
Dynamic Analysis = Upload of the file to the cloud for analysis
Capacity Handling = Store file and resubmit if file submission limit exceeded
Local Malware Analysis = Local ClamAV signature scanning

## Slide 85: Malware & File Use Case (cont.)
Block malicious Office, Executable, and PDF files transferred over HTTP

## Slide 86: Malware & File Use Case (cont.)
Block malicious Office, Executable, and PDF files transferred over HTTP

## Slide 87: Malware & File Use Case (cont.)
Block malicious Office, Executable, and PDF files transferred over HTTP

## Slide 88: Access Control Policy -- Revisited
Malware & File policy is applied on a per ACP rule basis.

## Slide 89: SSL Policy

## Slide 90: SSL Policies
Controls how and what encrypted traffic is inspected and decrypted
Simple policy blocks all encrypted traffic that uses a self-signed certificate.
Actions are:
  Decrypt – Resign: Used for SSL decryption of public services (Google, Facebook, etc.)
  Decrypt – Known Key: Used when you have the certificate’s private key
  Do not decrypt
  Block
  Block with reset
  Monitor
Many actions can be taken on encrypted traffic without decryption by inspecting the certificate, DN, cert status, cipher suite, and version (all supported by FTD).

## Slide 91: Noob Guide to SSL Encryption for HTTPS
Computers agree on how to encrypt.
  Client’s browser attempts to connect to SSL port on server. It sends a preferred Key, Cipher, Hash, (AKA Cipher Suite) and SSL version to server. (Client also sends a random number that will be used to create a master secret code.)
  Server responds with what Cipher Suite and SSL version it can do.
Client’s browser requests web server identity.
Server sends certificate to the client.
Browser checks whether SSL Certificate is trustworthy.
  Is certificate self-signed or signed via certificate authority that the client computer trusts.
Browser sends a “Start Encrypting” message to server. (Note: This is the last unencrypted transmission.)
Server sends back “Start Encrypting”, digitally signed ACK, to start session.
Encrypted data is shared.

## Slide 92: Basic 4 Use Cases for SSL
Known Key
Unknown Key
Don’t Decrypt
Block

## Slide 93: Basic 4 Use Cases for SSL (cont.)
Known Key
  Install server’s private key into NGFW.
  NGFW will then decrypt, inspect, and re-encrypt with server’s key.
Unknown Key
Don’t Decrypt
Block

## Slide 94: Basic 4 Use Cases for SSL (cont.)
Known Key
Unknown Key
  Install trust of NGFW as CA in workstations.
  Create NGFW key.
  Decrypt SSL, inspect, and then re-encrypt with NGFW’s key.
Don’t Decrypt
Block

## Slide 95: Basic 4 Use Cases for SSL (cont.)
Known Key
Unknown Key
Don’t Decrypt
  Acknowledge SSL use but just pass through (supposedly).
Block

## Slide 96: Basic 4 Use Cases for SSL (cont.)
Known Key
Unknown Key
Don’t Decrypt
Block

## Slide 97: Create SSL Policy

## Slide 98: Create SSL Rule
For public servers (you don’t control)
For servers you control

## Slide 99: Assign SSL Policy to ACP

## Slide 100: Access Control Policy -- Revisited
SSL Policy is applied at the Access Control Policy level thus “affects” all policies/rules associated with the devices assigned to this ACP.

## Slide 101: SafeSearch/YouTube EDU

## Slide 102: What is SafeSearch/YouTube EDU?
SafeSearch is an “app” that certain search engines provide that will filter out inappropriate content from search results.
YouTube EDU is an extension of the SafeSearch feature that targets YouTube content.
SafeSearch can be manually turned on within google.com. (Per browser, per device, per user)
  It could then also be turned off by the end user.

## Slide 103: Configure ACP Rule for SafeSearch
In an ACP Rule, on the Applications tab, click the SafeSearch link.
Enable Safe Search.
Choose what to do about search engines that don’t support Safe Search.
Build remaining criteria for ACP rule to match traffic you want.

## Slide 104: Supported Search Engines for SafeSearch

## Slide 105: Warning that it is a 2-step process

## Slide 106: Configure SSL Policy Rule for SafeSearch
Create SSL Policy Rule.
On the Applications tab search for and select “search engine” category.
Rule’s action must be “Decrypt – Resign”.

## Slide 107: Associate SSL Policy to ACP
More information about SSL Policies will be provided later in the lecture.

## Slide 108: SafeSearch Permanently Enabled
Even if user tries to disable SafeSearch the page will reload and SafeSearch will remain “on”.

## Slide 109: Configure ACP Rule for YouTube EDU
Create an ACP Rule and on the Applications tab click the YouTube EDU link.
Enable YouTube EDU.
Enter your YouTube EDU ID.

## Slide 110: Configure SSL Policy Rule for YouTube EDU
Create an SSL Policy Rule.
On the Applications tab click search for and select YouTube Applications.

## Slide 111: Associate SSL Policy to ACP
More information about SSL Policies will be provided later in the lecture.

## Slide 112: YouTube Blocked Content Message

## Slide 113: Order of ACP rules is Important!

## Slide 114: Network Discovery

## Slide 115: Network Discovery Customization
By default Network Discovery examines ALL traffic traversing the FTD (i.e. 0.0.0.0/0 and ANY zone.)
Create new network discovery rule or modify default to meet you needs.
Can create exclusion rules to single out exceptions.

## Slide 116: Network Discovery Results

## Slide 117: Host Profile of Discovered Host

## Slide 118: Host Profile of Discovered Host (cont.)

## Slide 119: Uses of Discovered Information
Firepower Recommendations for customized Intrusion Policies.
Indications of Compromise.
User to Machine correlation.
Which applications are being used on this network.
Vulnerabilities report for each host.

## Slide 120: Intrusion Policy

## Slide 121: Intrusion Policies
Controls how IDS/IPS inspection is performed on network traffic.
Cisco Talos maintained base policies (the default policies):
  Balanced Security and Connectivity: Default and recommended
  Security Over Connectivity: More rules enabled, deeper inspection (at a cost)
  Connectivity Over Security: Fewer rules enabled, only most critical rules block
  Maximum Detection: Favors detection over rated throughput. Use only if TAC says so.
  No Rules Active: Disable SNORT for this ACP rule.
Individual rules can be set to generate events, drop and generate events, or disabled.
Layers allow for grouping of settings/rules for easier management
Complex policies can contain multiple layers and multiple levels of inheritance.

## Slide 122: Licensing

## Slide 123: Intrusion Policy to ACP Rule Association

## Slide 124: Create Intrusion Policy

## Slide 125: Intrusion Policy’s are Highly Customizable

## Slide 126: Firepower Recommendations

## Slide 127: Firepower Recommendations (cont.)

## Slide 128: Access Control Policy -- Revisited
Intrusion policy is applied on a per ACP rule basis.

## Slide 129: Rate Limiting/QoS

## Slide 130: Create QoS Policy
Devices > QoS
Click New Policy
Give Name
Assign FTDs
Save

## Slide 131: Order of Match

## Slide 132: Caveats/Limitations
Max 32 QoS rules
Constrain rules by src/dest (routed) interfaces.
Rate limiting is enforced independently on each interface (not aggregated and/or differently based on src/dest interface pairs).
QoS rules can rate limit traffic by:
  Transport/network layer characteristics: IP address or geolocation, port, protocol
  Contextual information: Application control, URL filtering
  User information: realm, user, user group, ISE attribute
Ingress and Egress can be rate limited independently.

## Slide 133: FTD Packet Flow

## Slide 134: Packet Flow Through FTD

## Slide 135: Packet Flow Through FTD (cont.)
Packet arrives on the ingress interface.
Input counters incremented by NIC and periodically retrieved by CPU.
Software input queue (RX ring) is an indicator of packet load.
Overrun counters indicates packet drops (usually packet bursts)

## Slide 136: Packet Flow Through FTD (cont.)
If existing connection exists bypass Untranslate NAT and ACL steps. Process in Fastpath.
Otherwise:
If TCP packet but NOT SYN packet, drop and log.
Process through NAT to untranslate destination IP addresses, if applicable. Note: This is NOT the actual NAT phase. Just “un-NAT” enough to run through ACLs. ACL checks are done on the “untranslated” IP addresses.

## Slide 137: Packet Flow Through FTD (cont.)
If no Fastpath:
Check IP Reputation / Security Intelligence Lists.
  Drop packet if blacklisted.
Application Identification (think AVC)
  Attempt to identify and categorize packet to an application.
Enforce policy rules
  Note: Firepower policies don’t actually drop the packet. They flag the packet to be dropped and Lina drops the packet.
Generate an event log.

## Slide 138: Packet Flow Through FTD (cont.)
Perform Application Layer Gateway checks (think fixup)
Perform NAT translation (in preparation for exiting the FTD device):
  Translate the source and destination IP addresses in the IP header.
  Translate the port if performing PAT.
  Update header checksums
  More about the types of NAT later in this presentation (Auto vs. Manual).

## Slide 139: Packet Flow Through FTD (cont.)
Packet is “virtually” forwarded to egress interface. (Not actually forwarded yet.)
Egress interface is determined first by translation rule or existing connection entry THEN the routing table
If NAT does not divert to the egress interface, the global routing table is consulted to determine the egress interface.
Once at egress interface, route lookup is performed.
Only routes pointing out of selected egress interface are considered.
  If the destination is not routable out the selected egress interface the packet is dropped.
Once L3 route is found L2 resolution is performed (i.e. ARP).
  If L2 resolution fails the packet is dropped.
Packet is transmitted on the wire and interface counters will increment.
  Underrun counters indicates drops due to egress interface oversubscription. (TX ring is full.)

## Slide 140: Reports and Dashboards

## Slide 141: Dashboards

## Slide 142: Dashboards (cont.)

## Slide 143: Report Templates

## Slide 144: Report Designer

## Slide 145: Generated Reports

## Slide 146: Generated Reports (cont.)

## Slide 147: Device Monitoring

## Slide 148: Management Monitoring

## Slide 149: VPN on FTD

## Slide 150: VPN on FTD
Site to Site (only)
Remote access (i.e. AnyConnect) not in v6.1.
Topologies:
Point to Point
Hub and Spoke
Full Mesh

## Slide 151: Point to Point Example

## Slide 152: Hub and Spoke Example

## Slide 153: Full Mesh Example

## Slide 154: Verification and Monitoring VPN

## Slide 155: Application Program Interface (API)

## Slide 156: API on FMC
Issue API calls to FMC
  API-Explorer
  External script (python, perl)
Cannot “push” to FTD (yet)
Good for regular/mass repetitive changes (PUT or POST or DELETE)
Great for regularly retrieving JSON formatted information (GET)
Use to updated 3rd party and/or in-house external monitoring tools
A username can only uniquely log into FMC via HTTPS once. If that username attempts to log in a 2nd time their 1st connection will be logged out.
Creation of a special “API User” might be best to avoid HTTPS access collisions since API calls and web page calls are treated the same.

## Slide 157: API Explorer
https://<fmc IP>/api/api-explorer

## Slide 158: API Explorer (cont.)

## Slide 159: Exporting a Generic Script

## Slide 160: Standalone Scripting
Import the needed libraries
Provide the FMC IP/hostname
Either pass the username/password as arguments when running the script or embed them into the script.
Either use/import certificates to communicate with FMC or disable SSL verification (as shown).

## Slide 161: Standalone Scripting (cont.)
Configure the API call path with any parameters desired.
Like shown in step 4, either use/import certificates to communicate with FMC or disable SSL verification (as shown).

## Slide 162: Standalone Scripting (cont.)

## Slide 163: Upgrade ASA to FTD Code

## Slide 164: Caveats
Read the release notes!
Supported ASA Platforms: ASA 5506-X, ASA 5506H-X, ASA 5506W-X, ASA 5508-X, ASA 5512-X, ASA 5515-X, ASA 5516-X, ASA 5525-X, ASA 5545-X, and ASA 5555-X
Minimum ASA version: 9.6.1 (or later)
Minimum ROMMON Mode: 1.1.8
Note: 5585 will NOT support FTD!
Remember this is a complete format and reimage. All files, codes, images, configs on the ASA will be lost during this process!

## Slide 165: Install Boot Image
Enter ROMMON
  Press ESC when prompted.
Configure ROMMON Variables
  “set” will list variables and their values.
  Variables are CaSe SeNsiTiVe!
  There is no “space” between variable, equal sign, and value.
“sync” to save changes.
Ensure connectivity (i.e. ping) to the TFTP server.
Note: Some ASA appliances require a “.cdisk” file and others use a “.lfbff” file.

## Slide 166: Install Boot Image (cont.)
Issue “tftpdnld” command to start the downloading of the image.

## Slide 167: Install Boot Image (cont.)
ASA will reboot.
Be ready to press ESC to boot the boot image!!!
This is the trickiest part of this upgrade since you have to be ready to press ESC or the ASA will just boot up its standard image and you’ll have to start over!

## Slide 168: Install FTD Image
Issue “setup” command.
Fill out questionnaire to provide access to FTP/HTTP server where FTD image resides.
Apply changes and reboot.

## Slide 169: Install FTD Image (cont.)
Issue “system install” command.
Confirm erasure.
If needed, provide credentials for FTP server.

## Slide 170: Install FTD Image (cont.)
Confirm performing upgrade.
Once done, reboot.

## Slide 171: Set up Firepower Device Manager

## Slide 172: Firepower Device Manager
On box/locally managed
Use when no FMC is available/reachable.
Switching from “locally managed” to “FMC managed” WILL erase the local configuration!

## Slide 173: Accessing the GUI
Access, via HTTPS, the device’s management IP.
Log in using admin account. (By default this is admin/Admin123.)

## Slide 174: Take the Defaults, or not.
The Defaults
Interfaces:
  0/1 is “inside”
  0/2 is “outside”
  Management is assumed to be on “inside” LAN.
IPs:
  Management: 192.168.45.45
  Inside: 192.168.45.0/24
  Outside: DHCP
DHCP Pool
  192.168.45.0/24 pool for “inside”.
Accounts:
  admin/Admin123
Note: Click “Skip device setup” to build it to your design.

## Slide 175: Eval Licensing

## Slide 176: Disable DHCP and Remove DHCP Pool

## Slide 177: Configure to your liking
Set data plane interface names.
Set data plane interface IPs.
Configure routing. (Default route at least if no DHCP for “outside”.)
Assign interfaces to zones.
Configure NAT.
Don’t forget to Deploy!

## Slide 178: Cisco Healthcheck and Tuning Services

## Slide 179: Cisco Healthcheck & Tuning Services – Subject Matter Expert
Product SKU (applicable) | Services SKU (s) | Segment | Geo | Lifecycle
All security Products | ASF-CORE-G-SSME1L (AMER – Travel Inc) ASF-CORE-G-SSME1W (APJC & EMEA, No Travel) ASF-CORE-G-SSME1I (APJC & EMEA, International Travel) Transactional AS-SEC-SME | All | All | Plan & Build
Typical skill set or expertise of Cisco personnel providing services is as follows:
• In-depth Subject Matter Expertise knowledge of the selected Cisco Security Product and varying knowledge from general to expert levels with other Cisco and 3rd Party Security Product technologies.
• Expertise in integrating, operating, and managing the Cisco Security Product within diverse Customer environments providing an end-to-end professional security experience.
• Ability to analyze security requirements and specify hardware and software requirements, including security management tools.
• Ability to understand, identify and mitigate security risks that affect compliance requirements.
• Knowledge in migrating from existing products to the selected Cisco Security Product.
• Experience in developing an in-depth security architecture.
• Assessment of the network’s readiness to deploy a new security solution, including the existing IT infrastructure, security devices, software operations, and security management procedures.
• Ability to assist Customer in the planning, design, and implementation of security solutions.
• Proficiency in the development of detailed security designs, including network diagrams, system rules and reports, and sample software configurations for protocols, policies, and features.
• Assistance in testing a pilot security solution to confirm that expected performance is attained.
• Development of an implementation strategy and plan detailing the requirements for solution deployment, integration, and management.
• Expertise in support of custom installation, configuration, testing, tuning, and integration of a security solution.

## Slide 180: Cisco Security Migration Services (ASA/Firepower)
SKU (s) | Segment | Geo | Lifecycle
AS-SEC-CNSLT (US, CAN, EUROPE) AS-SEC-CNSLT-A (APJC AS-SEC-CNSLT-L (Emerging) | All | All | Plan & Build
Security Migration Services can help migrate from a current security environment to a more innovative security infrastructure that provides proactive ongoing protection, and gives a clear understanding of the risks in the current environment and outline the best possible migration strategy.
Transactional ASA Migration Services
The transactional ASA Migration services covers more complex, enterprise level firewall configuration migrations, including PIX, Check Point, and Juniper firewalls to the ASA platform. These services cover multiple platforms, enterprise-wide features, functionality and complexity.
These services are SOW based, custom scoped and delivered.
Benefit from Cisco Migration Services
The right level of security provides the confidence to freely engage in new business opportunities and initiatives with customers, partners, and employees. Available either on site or remotely, Cisco Security Migration Services deliver an array of benefits, including:
Improved methods to reduce disruptions and the risks of costly rework during and after migration
Efficiencies to help you increase the capabilities from your investment through thorough plan reviews
Focused support and guidance through crucial transition periods
Improved network uptime during migration through the use of proven processes and tools
Reduced risks of lost business before, during, and after migration
Accelerated migration to advanced security platforms
Ongoing support and knowledge transfer when requested

## Slide 181: Deployment Services for Firepower Solutions
Product SKU | Services SKU(s) | Segment | Geo | Lifecycle
Firepower ordering guide | ASF-CORE-FW-DEP (AMER) ASF-CORE-FW-DEP-NT (APJC, EMEAR No travel) ASF-CORE-FW-DEP-IT (APJC & EMEA International Travel) | All | All | Plan & Build
This Service covers the following managed devices and Firepower Solution components:
One (1) standalone or one (1) High-Availability pair management solution from the following options:
  FireSIGHT Management Center (FMC)
  Firepower Management Center (FMC)
Up to ten (10) total managed devices from the device platform types listed below, of which four (4) may be Firepower Threat Defense instances:
  FirePOWER Appliances
  Virtual FirePOWER Appliances
  FirePOWER Modules (ASA or ISR)
  Firepower NGFW Appliances
  Firepower Threat Defense (FTD) on ASA Appliances
  Virtual Firepower Threat Defense

## Slide 182: Thank you!
Additional Information:
CiscoLive BRKSEC 2020 (Firewall Deployment FTD)
CiscoLive BRKSEC 2050 (ASA Firepower NGFW typical deployment scenarios)
Important Links:
Quick Start Guide
Release Notes
Configuration Guide
Questions?